## Slide 1
Default vs. Preset Values
SystemC CCI WG
Vishal Goel
Texas Instruments Inc.
Jan 2011
Notes: <number>
<number>

## Slide 2
Default vs. Preset values of a parameter
Demonstrate relative precedence of default (supplied to parameter constructor) and preset (via name-based broker access prior to construction) values.
User module specifies some default value for different parameters in respective constructors.
Set one of the parameters to a different value from a tool/configurator, before the user module’s construction.
Report the various parameters’ name (hierarchical) and value in the constructor and at the end of simulation.
Demonstrate the reporting of unconsumed preset values with filtering functions.
Notes: <number>
<number>

## Slide 3
Example Sequence Diagram
sim_ip: simple_ip
cfg_ip: config_ip
param_1= 10
@Construction
cci_param<int> param_1(“param_1”, 1);
param_1, param_2 ‘Owner’ module
EXTERNAL module updating param_1
cci_param<int> param_2(“param_2”, 2);
param_2= 2
m_broker.set_preset_cci_value(“sim_ip.param_1”, “10”);
preset value takes precedence over default value (see param_1)
m_broker.set_preset_cci_value(“cfg_ip.param_implicit_3”, “3”);
Unconsumed preset value
Notes: <number>
<number>

## Slide 4
Contd.
sim_ip: simple_ip
cfg_ip: config_ip
@Simulation
param_1, param_2 ‘Owner’ module
EXTERNAL module updating param_1
m_cci->set_init_value(“sim_ip.param_1”, “5”);
preset value set after construction does not affect parameter value
m_broker.set_init_value(“param_implicit_1”, “1”);
m_broker.set_init_value(“foo.bar.baz.param_implicit_2”, “2”);
Unconsumed preset values
Notes: <number>
<number>

## Slide 5
Expected Output
(ex05_Default_and_Preset_Value.log)
SystemC Simulation
Info: cfg_ip: @0 s, Attempting to setup config_ip to 10 before IP construction
Info: cfg_ip: @0 s, Setting up sim_ip.param_1's preset value to 10
Info: cfg_ip: @0 s, Setting up cfg_ip.param_implicit_3's preset value to 3
Info: sim_ip: @0 s, @Ctor: Value of sim_ip.param_1 is 10 (Default value Specified: 1)
Info: sim_ip: @0 s, @Ctor: Value of sim_ip.param_2 is 2 (Default value Specified: 2)
Info: sc_main: Begin Simulation.
Info: cfg_ip: @0 s, execute: [EXTERNAL] Current value of sim_ip.param_1 is 10
Info: sim_ip: @0 s, Setting up param_implicit_1's preset value to 1
Info: sim_ip: @0 s, Setting up foo.bar.baz.param_implicit_2's preset value to 2
Info: sim_ip: @0 s, Unconsumed preset cci values:
cfg_ip.param_implicit_3
foo.bar.baz.param_implicit_2
param_implicit_1
Info: sim_ip: @0 s, Ignore unconsumed values cfg_ip.*
Info: sim_ip: @0 s, Unconsumed preset cci values result:
Notes: <number>
<number>

## Slide 6
Contd.
foo.bar.baz.param_implicit_2
param_implicit_1
Info: sim_ip: @0 s, Unconsumed preset cci values with value = 2:
foo.bar.baz.param_implicit_2
Info: sc_main: End Simulation.
Info: sim_ip: @Dtor: Value of sim_ip.param_1 is 10
Info: sim_ip: @Dtor: Value of sim_ip.param_2 is 2
Notes: <number>
<number>