## Slide 1
Specifying Parameter Value via a Configuration File SystemC CCI WG
P V S Phaneendra
CircuitSutra Technologies Pvt. Ltd.
Aug 2011
Notes: <number>
<number>
<number>
<number>

## Slide 2
Specifying Parameter Values via a Configuration File
Objective of the present example is to demonstrate the following :
  Understand the precedence between the default, preset and set values
  Processing configuration file to establish preset values
2
Notes: <number>
<number>
<number>
<number>

## Slide 3
Include the “cci_configFile_Tool.h”
Include the configuration file as shown below :
cci_configFile_Tool configTool("configFileTool"); configTool.config("Configuration_File.txt");
Configuration File
Reads the file that stores the preset values
Ex: param_owner.mutable_int_param 10
param_onwer.mutable_string_param preset
param_owner.mutable_int_param 15
Within sc_main
Create an instance of the class that reads the configuration file within the sc_main function.
Cci_configFile_Tool reads name-value pairs from the configuration file and assigns to the respective parameters accordingly.
3
Example Illustration
Notes: <number>
<number>
<number>

## Slide 4
Class cci_configFile_Tool Implementation
Configuration File
Reads the file that stores the preset values
Ex: param_owner.mutable_int_param 10
param_onwer.mutable_string_param preset
param_owner.mutable_int_param 15
Class cci_configFile_Tool is a simple C++ class
Get handle m_broker to the global broker
m_broker(cci::get_global_broker(mToolOriginator);
Within API, inline void config (const char* filename), the function reads the file Configuration_File.txt line by line using an iterator.
It assigns the prest values to the cci-parameters read from the file using the broker m_broker
m_broker.set_prest_value(it->first.c_str(), cci::cci_value::from_json(it->second.c_str()));
String passed from the configuration file containing parameter_name
String passed from the configuration file containing parameter_value
Define a cci::cci_originator instance mToolOriginator
4
Example Illustration (contd.. 1)
Notes: <number>
<number>
<number>

## Slide 5
Parameter_Configurator
Integer Parameter Value : int_param.get() : 10
Float Parameter Value : float_param.get() : 123.45
String Parameter Value : str_param.get() : preset
Get references of the integer, float and string cci-parameters
cci::cci_param_handle int_param_ptr =
m_broker.get_param(“param_owner.mutable_int_param”);
cci::cci_param_handle float_param_ptr =
m_broker.get_param(“param_owner.mutable_float_param”);
cci::cci_param_handle str_param_ptr =
m_broker.get_param(“param_owner.mutable_string_param”);
Set new values to ‘integer’ and ‘string’ type parameters
Integer Parameter Value : int_param.set_cci_value(cci_value(“20”))
String Parameter Value : str_param.set_cci_value(cci_value::from_json(“configure”))
@ 0 ns
Integer Parameter Value : int_param.get_value() : 20
Float Parameter Value : float_param.get_value() : 123.45
String Parameter Value : str_param.get_value() : configure
@ 5 ns
Parameter_Owner
5
Example Illustration (contd.. 2)
Notes: <number>
<number>
<number>

## Slide 6
Precedence of Prest, Default & Set Values
Parameter#1
Parameter#2
Preset value available
Preset value not available
Default value available
Default value available
Before instantiation of the cci-parameter
Default value over-ridden by the preset value
Preset value has the highest precedence
Default value set
During construction of the cci-parameter
Set new value using direct assignment or JSON
Set new value using direct assignment or JSON
New value set
New value set
After construction of the cci-parameter
7
Notes: <number>
<number>
<number>

## Slide 7: Expected Output (ex17_Specifying_Parameter_Value_via_a_Configuration_File.log)
SystemC Simulation
ConfigFile_Api: Applying preset value of param 'param_owner.mutable_int_param' to '15'
ConfigFile_Api: Applying preset value of param 'param_owner.mutable_string_param' to '“preset"'
Info: param_owner: @0 s, [OWNER C_TOR] : Int Parameter Value : 15
Info: param_owner: @0 s, [OWNER C_TOR] : Float Parameter Value : 123.45
Info: param_owner: @0 s, [OWNER C_TOR] : String Parameter Value : preset
Info: param_setter: @0 s, [CFGR C_TOR] : Integer parameter exists
Info: param_setter: @0 s, [CFGR C_TOR] : Float parameter exists
Info: param_setter: @0 s, [CFGR C_TOR] : String parameter exists
Info: param_setter: @0 s, @ 0 s
Info: param_setter: @0 s, [CFGR] : Set integer parameter value to '20'
Info: param_setter: @0 s, [CFGR] : Set string parameter value to 'configure'
Info: param_owner: @5 ns, @ 5 ns
Info: param_owner: @5 ns, [OWNER] : Int Parameter Value : 20
Info: param_owner: @5 ns, [OWNER] : Float Parameter Value : 123.45
Info: param_owner: @5 ns, [OWNER] : String Parameter Value : configure
Notes: <number>