## Slide 1: Simple Immutable Parameters SystemC CCI WG
Vishal Goel
Texas Instruments Inc.
Feb 2011
Notes: <number>

## Slide 2: Simple Immutable Parameter
Demonstrate use of simple immutable parameters
User module specifies variables as immutable
Use Case 1:
  Define a parameter with default value
  Once this value is set, any attempt to change the parameter at run time will fail.
Use Case 2
  Define an initial value for a parameter; before parameter construction.
  This value will take precedence over default (constructor) value of the parameter; as well as; any attempt to change the parameter at run time will fail
Notes: <number>

## Slide 3: Example Sequence Diagram (UC-1)
sim_ip: simple_ip
cfg_ip: config_ip
@t = 0ns
cci_param<int,immutable_parameter>
param_1(“param_1”, 1);
param_1 = 10;
param_1 ‘Owner’ module
EXTERNAL module updating param_1
Default value is ignored. param_1 remains “100” (Ref: example5)
Set up init value to 100
Attempt to update param_1 value fails. param_1 remains “100”
@t = 10ns
m_broker.set_preset_cci_value( "sim_ip.param_1", cci::cci_value::from_json("100"));
Notes: <number>

## Slide 4: Example Sequence Diagram (UC-2)
sim_ip: simple_ip
cfg_ip: config_ip
@t = 0ns
@t = 20ns
param_2 = 20;
param_2 ‘Owner’ module
EXTERNAL module updating sim_ip.param_2
Default value will be used. param_2 = 2
Internal updates are also rejected.
param_2_handle.set_cci_value( cci_value("200"));
@t = 30ns
cci_param<int,immutable_parameter>
param_2(“param_2”, 2);
External updates are rejected.
Notes: <number>

## Slide 5: Expected Output (ex04_Simple_Immutable_param.log)
SystemC Simulation
Info: cfg_ip: @0 s, Attempting to setup config_ip to 100 before IP construction
Info: cfg_ip: @0 s, Set init-value of sim_ip.param_1 to 100
Info: sim_ip: @0 s, @Ctor: Default value specified for sim_ip.param_1 is 1
Info: sim_ip: @0 s, @Ctor: Default value specified for sim_ip.param_2 is 2
Info: sim_ip: @0 s, @Ctor: param_1 mutable type is immutable
Info: sim_ip: @0 s, @Ctor: param_2 mutable type is immutable
Info: sim_ip: Info: Ctor: immutable param:param_1 = 100 (expected)
Info: sim_ip: Info: Ctor: immutable param:param_2 = 2 (expected)
Info: sc_main: Begin Simulation
Info: sim_ip: @0 s, execute method is testing Use Case 1
Info: sim_ip: Info: @Run: param_1 = 100 (expected)
Info: sim_ip: @10 ns, @Run: Assign new value (10) to sim_ip.param_1
Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter (sim_ip.param_1) is immutable. In file: <removed by verify.pl> In process: sim_ip.execute @ 10 ns
Info: sim_ip: Info: @Run: param_1 = 100 (expected)
Notes: * There are lot more messages coming from CCI infrastructure code; the report includes only user messages (not from cci infra)
<number>

## Slide 6: Contd..
Info: sim_ip: @10 ns, execute method is testing Use Case 2
Info: cfg_ip: @20 ns, Attempting to set value of 'sim_ip.param_2' to 200
Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter (sim_ip.param_2) is immutable. In file: <removed by verify.pl> In process: cfg_ip.execute @ 20 ns
Info: sim_ip: Info: @Run: param_2 = 2 (expected)
Info: sim_ip: @30 ns, @Run: Assign new value (20) to sim_ip.param_2
Error: /Accellera/CCI/SET_PARAM_FAILED: Parameter (sim_ip.param_2) is immutable. In file: <removed by verify.pl> In process: sim_ip.execute @ 30 ns
Info: sim_ip: Info: @Run: param_2 = 2 (expected)
Info: sc_main: End Simulation